## Slide 1: Vector & Array Processors
How to process more data at a time…

## Slide 2: Some Taxonomy (Flynn’s)
Think about a CPU as a box that takes in instructions and data and yields results. Ignoring multi-core and SMP for a moment…
CPU/Core
Data
Instructions
Results

## Slide 3: Flynn’s Taxonomy
SISD – single instruction, single data item - classic processors
SIMD – single instruction multiple data – used in Vector Processors & GPUs
MISD – multiple instructions operating on the same data (fault tolerance)
MIMD - multiple instructions, multiple data - multi-core super scalar, distributed systems

## Slide 4: Key Concept
In order for code to be run in parallel, loop iterations must be independent.
for (int i=0;i<N;i++)
a[i] = a[i-1] + a[i-2];
This code is not easily vectorizable. Some special hardware can handle this.

## Slide 5: Data Parallelism
It is not uncommon that we need to do the same operations on a lot of pieces of data:
for (a in array)
doSomething(a)
Examples: Image/sound/video processing, matrix operations, AI

## Slide 6: Data Parallelism
It is not uncommon that we need to do the same operations on a lot of pieces of data:
for (a in array)
doSomething(a)
Examples: Image/sound/video processing, matrix operations, AI
How can we “doSomething” on more than one “a” at a time?

## Slide 7: Two Options
Vector Processor – we have 1 ALU. At time 0, we load item 0. At time 1, we load item 1 and process item 0. At time 2, we load item 2, process item 1 and store item 0. Essentially, we pipeline the items. Think of doing laundry at home with 1 washer and 1 dryer.
Array Processor – we have N ALUs. To process a batch (image, matrix, sound file, whatever), we break it up into N sections. We load N items. We do the operations on all N items. Then we save all N items out. Example – taking ALL of the laundry to the laundromat.
Tradeoffs?

## Slide 8: Does it matter?
From a certain perspective, no.
The problems that we are looking at have some things in common:
Few/no inter-array dependencies
Little/no flow control outside of the array loop
Simple array walking (not random indexing)
Vector and Array processors are good at the same problems.

## Slide 9: Vector Processing

## Slide 10: Vector processors sound like CPUs!
Some key differences:
No/few inter-array dependencies
With a known stride, we can accurately prefetch correctly
Little control flow
Short “programs” ease instruction memory bandwidth requirements:
Can live in cache?
Much simpler than the out of order, pipelined “normal” CPUs.
Result: very deep pipelines are OK
Stride – distance between “batches” of data

## Slide 11: Making a vector processor
Looping is implicit in a vector processor.
We need a few control registers:
VLEN – how many total data items we need to work on
VSTR – how many words between data items (stride)
VMASK – allows us to “turn off” updates to a register (as we will see)

## Slide 12: Implicit Loop
When you set VSTR and VLEN, the vector processor starts running your code. Inside the vector processor, there is an implicit loop:
for (a  0 to VLEN) {
// vectored loads and stores automatically use “a”
a+=VSTR;
}

## Slide 13: Imaginary example: C=A+B
Scalar Code
MOVE 0,R1
loop: LOAD (A+R1), R2
LOAD (B+R1),R3
ADD R2,R3, R4
STORE R4,(C+R1)
ADD 1,R1
BLE 100, loop
Vector Code
MOVE 100,VLEN
MOVE 4,VSTR -- 4 byte integers
VLOAD A,VR0
VLOAD B,VR1
VADD VR0,VR1,VR2
VSTORE C, VR2

## Slide 14: A note about memory
Because vector processors are deeply pipelined, they can issue a lot of load/store combinations in a short time and will very quickly saturate memory.
Vector processors work best when the amount of work to be done on each element is the same as or more than the work to load/save data.
Carefully laying out your data in memory so that different banks of RAM hold successive data items can help, too!

## Slide 15: If only everything were quite this simple…
Remember “few/no inter-array dependencies”?
In some cases, there are data items used by more than 1 calculation.
For example, consider 1 dimensional blurring (2D is just an extension of the same idea).
The value of o[j] = (i[j-1]+i[j] + i[j+1])/3 (o = output, i = input).
This is called chaining. Vector processors typically support it, but now we have a problem. We can’t use a simple pipeline. Why?

## Slide 16: Does the diagram help?
In[0]
In[1]
In[2]
Out[0]
Out[1]
Out[2]
Add
Div
Add
Div
Add
Div

## Slide 17: Memory can’t serve two (or three) masters
Typically, memory can only be read by one unit at a time
But multi-ported memory can be used.
In this case, we need 3 ported memory in order to pipeline this process fully.
Unless… what if we had some limited amount of memory to retain previous answers?

## Slide 18: Chaining
Chaining is the concept of one vector iteration or functional unit forwarding data to another iteration.
This, of course, has a cost – the hardware must detect or be instructed that this needs to happen and the data must be retained for future iterations (storage required).

## Slide 19: More “fun” with memory
What if we need to reference memory, but we want to either load or store indirectly:
A[B[i]] = C[D[i]] + 1
This is called a scatter (output) and gather (input) operation.
There is hardware for this in most vector processors.

## Slide 20: A little more…
What if we want to only operate on certain data items?
A[i] = B[i] / C[i], if C[i] != 0
That’s what the VMASK is for.
We can mask out the records where C[i] is 0.
VMASK = C[i] != 0;
Does this remind you of something? Maybe from ARM?

## Slide 21: One more masking example
What if I want to do something like this:
if (a[i] > b[i])
c[i] = a[i]-b[i];
else
c[i] = b[i] – a[i];
Becomes:
VMASK = A>B
C = A-B
VMASK = !VMASK
C = B-A

## Slide 22: History of Vector Processors
Vector processing was popular in the 1960’s-1980’s.
At that time, transistors/CPU were very low. Using every functional element (load, store, ALU) every cycle was an important way to improve performance.
The most famous vector processors were the Cray-1 and Cray X-MP.

## Slide 23: Array Processing

## Slide 24: More than one thing at a time…
As the manufacturing of chips got better, designers had more transistors to work with.
The limit of a single Load/ALU/Store processing element combination was overcome.
Array Processors work very much like Vector Processors, but incorporate multiple processors.

## Slide 25: Vector Processors Vs Array Processors
Vector Processor
Load 0
Load 1
Load 2
Math 0
Math 1
Store 0
Time
Array Processor 1
Array Processor 2
Array Processor 3
Array Processor 4
Load 0
Math 0
Store 0
Load 1
Math 1
Store 1
Load 2
Math 2
Store 2
Load 3
Math 3
Store 3
Time
Less hardware
More hardware

## Slide 26: Making a array processor
We need N*M registers to work on N items at a time.
M is the number of operands we can have.
Consider C[i] = A[i] + B[i]. We need 3 (M) registers for each N.
We need more ALUs and more memory bandwidth.
We need the same control registers:
VLEN – how many total data items we need to work on
VSTR – how many words between data items (stride)
VMASK – indicates which of the registers (bitwise) to work on.

## Slide 27: What happened to Array Processors?
In a sense, nothing – they still exist, as we will see next week.
You don’t typically see computer systems that are just array processors, though.
Illiac4 and the Aspex ASP Linedancer are examples of array processors (both retired).

## Slide 28: Programming Models/Tools
How can we write code for these models?

## Slide 29: Let’s think about a piece of simple code
for (int i=0;i<N;i++)
c[i] = a[i] + b[i];
Load
Load
Add
Store
Load
Load
Add
Store
Iteration 1
Iteration 2

## Slide 30: We can think about this as a simple in-order
Load
Load
Add
Store
Iteration 1
Load
Load
Add
Store
Iteration 2
Or out of order
Load
Load
Add
Store
Iteration 1
Load
Load
Add
Store
Iteration 2
This is, essentially, the CPU unrolling the loop for us

## Slide 31: Or a vector processor (SIMD)
LOAD A  V1
LOAD B  V2
ADD V1, V2  V3
STORE V3  C
Ignoring stride, masks, etc…

## Slide 32: Or a multi-core CPU/Array Processor
Load
Load
Add
Store
Load
Load
Add
Store
Iteration 1
Iteration 3N/4
Load
Load
Add
Store
Iteration N/4
Load
Load
Add
Store
Iteration 2N/4

## Slide 33: Loop Unrolling
for (int i=0;i<N;i++)
c[i] = a[i] + b[i];
can become:
for (int i=0;i<N;i+=4) {
c[i] = a[i] + b[i];
c[i+1] = a[i+1] + b[i+1];
c[i+2] = a[i+2] + b[i+2];
c[i+3] = a[i+3] + b[i+3];
}
Why do we (the compiler, really) do this? Because looping (branches, compares) are overhead – “useful” work is not getting done.
Notice how the unrolled code would be perfect for an array or a vector processor.
Why don’t we unroll the loop completely (i.e. make N copies of the row)?

## Slide 34: Execution Model
If we have SPMD (single program, multiple data), where can we execute it?
We have the best of all worlds with this case –
We can run it in a loop on an SISD (single core cpu/vector processor)
We can run it on MIMD (multi-core)
We can run it in an array processor (SIMD)
Because it is the same code and we are applying it to many pieces of data, we can run it anywhere. So long as the compiler can unroll the loop for us.
This model has another name:
SPMD: Single Program, Multiple Data

## Slide 35: Hybrids – SIMD in modern ISAs
Or “why have I never heard of Array or Vector Processors?”

## Slide 36: CPU Extensions
So far, we have discussed Vector/Array processors as independent entities. In reality, they aren’t made that way anymore.
Today, we add these capabilities to more general CPUs like those in your laptop/desktop.
This all started with “multimedia” – graphics and sound on PCs.

## Slide 37: Multimedia
Multimedia was THE THING in the mid 90’s.
Remember, the internet was SLOW. Transferring “big” amounts of data was CDs or sneaker net.
CPUs were just becoming superscalar and pipelining was new (on the desktop).
DOOM (the first one!) was new and “everyone” wanted videos and games on their PCs. The 100mhz chips of the day couldn’t keep up.

## Slide 38: MMX and 3DNow
Intel (MMX, 1997) and AMD (3DNow, 1998) reacted to this by adding new CPU instructions.
The instructions on PCs up until then been SISD – a single instruction working on a single data item.
MMX(Intel) & 3DNow (AMD)– single instruction, multiple data
One instructions, can perform the same operation on a range of data

## Slide 39: How does this work? (Control)
The big idea is to create instructions that work on multiple data items at once (like an Array Processor).
Instead of VLEN, we let the “general purpose” (non-MMX) part of the processor run a loop.
Instead of VSTR (stride), we assume that we will work on contiguous data.

## Slide 40: How does this work? (Registers)
MMX introduces 8 new 64-bit registers. Transistors were still expensive, so MM0-MM7 are the same SRAM as the floating-point registers; there is a mode for FP math and one for MMX.
One operation can work on 8 (byte), 4 (word), 2 (longword) or 1 (quadword) data items at a time.
The instruction tells the system what to do (operation) and how big the data items are.

## Slide 41: How well did this work?
Title | Speed-up
Audio | 
Audio Echo Effects | 5.9x
G.728 Code Book Search | 2.7x
DSP Kernels | 
Efficient Vector/Matrix Multiply Routine | 14.6x
Matrix Transpose | 2x
Dot Product - 16x16 -> 32 | 5x
Real FIR - 16 bit | 5x
Vector Arithmetic and Logic Operations | 6x
Graphics (2D) | 
Fractals with MMX Technology | 1.5x
Graphics (3D) | 
Advanced Procedural Texturing | 10x
3D Bilinear Texture Mapping | 7x
3D Transform | 3.1x
Image Processing | 
2X 8-bit Image Scaling | 13.5x
Bilinear Interpolation | 3.9x
Median Filter | 3.8x
Alpha Blending | 8x
RGB -> YUV | > 10x
Speech Recognition | 
Viterbi Decoding | 2x
L1 Distance Measure | 3.3x
L2 Norm Distance Measure | 7.3x
Video | 
IDCT 2D 8x8 | 3.5x
Absolute Difference | 5x
Haar Transform - 2x2 | 2.2x
Get Bits | 2.4x
Video Loop Filter | 1.9
These are Intel’s numbers – your mileage may vary…

## Slide 42: SSE (Streaming SIMD Extenstions)
MMX was a good idea. SSE was the next generation (1999).
MM0 – MM7 were extended to 128 bit XMM0 – XMM7
Same idea – 16 bytes, 8 words, 4 long words, 2 quadwords
These registers are different from the FP registers.
New instructions were added to control caching – looping over a lot of data typically pollutes the cache.

## Slide 43: SSE2, SSE3, SSE4
SSE2 (2000) added the instructions from MMX to SSE. This frees the FP registers to be “just” FP registers, since developers should no longer write MMX instructions, but their SSE counterparts.
SSE3 (2004) adds the ability to add within a “package”
  In MMX, SSE, SSE2, you might have a1=a1+b1, a2=a2+b2
  In SSE3, you can now do: a1=a1+a2, a2=b1+b2
SSE4 (2006) adds several instructions requested by developers. No significant architectural change.

## Slide 44: AVX – 2011 (Advanced Vector eXtensions)
The 128bit SSE registers (XMM0-XMM15) are extended: YMM0-YMM15 are 256-bit registers; each one shares 128 bits with an XMM instruction.
MMX and SSE instructions were all two operand (A=A op B).
AVX introduces three operand (A=B op C) instructions; new opcodes “clone” SSE instructions to make a 3-operand version.
AVX instructions may reduce CPU clock rate to prevent overheating.

## Slide 45: AVX2 - 2013
Brings YMM support to most SSE and AVX instructions.
Adds more instructions.
Added gather (scatter-gather) support.

## Slide 46: AVX512 - 2016
Extends XMM0-7 (128-bit registers) and YMM0-YMM7 (256-bit versions) to ZMM0-7 (512-bit registers). ZMMx still shares bits with YMMx and XMMx.
Includes neural network and cryptography instructions! Adds prefetch for the scatter and gather instructions.
Not widely/completely supported. Newer CPUs (like Alder Lake) have even turned off AVX-512; this is an unusual design decision.

## Slide 47: Example – Chromakey (aka “green screen”)
When you watch a weather report and see a meteorologist in front of a map, it isn’t recorded that way. The person stands in front of a green (for example) screen. That image is recorded. Let’s call it Person.
A weather map is generated by some computer system. Let’s call it “Map”.

## Slide 48: Getting the Bitmask
We start by filling one register (XMM1, for example) with the color of the green screen in person 1.
We then loop over Person, loading each batch of pixels into a register (say, XMM3). We execute an instruction (PCMPEQB : Compare packed data for equal) – when XMM1’s value matches XMM3’s value, XMM1 becomes FFFF else it becomes 0000.
We now have a mask – a black and white silhouette of the meteorologist.

## Slide 49: Before and after

## Slide 50: Composing the Final Image
We now (re-load) Person. We execute PAND (and) between the mask and the person. That gives us either nothing (black) or the meteorologist.
We then load Map. We execute PANDN (not and) between the mask and Map to give us the map where the person is not or black (where the person is).
Finally, we POR the masked-Person with masked-Map.

## Slide 51: Results
Of course, we could do this one pixel at a time.
But the overhead of the loop would make it far too slow to be done live.
By using long registers, we can get array processing speed and work in realtime.

## Slide 52: Conclusion
Vector processors were an early attempt to optimize certain problems – repeated operations on the same data.
ALUs were too expensive to replicate
Array processors improved on vector processors by adding ALUs
Special purpose processors were not worth building, until recently.
Hybrid approaches have been in use for many years.