## Slide 1: Caches

## Slide 2
DRAM is not fast enough to keep our processors filled with instructions and data.
SRAM is too expensive to run our computers on.
What do we do?

## Slide 3
Consider this image.
There are 3 classes of books in this image.
The book he is reading
The stack of books next to him.
The shelves in the
back of the room

## Slide 4: Access Time and Size
In that image, how long would it take the man to get to a page:
In the book he is reading?
In the stack next to him?
In a particular book on the shelves?
How many books (approximately) are in each of the above categories?
Is this setup optimal?

## Slide 5: Locality
This setup works for him because he likely has one or both types of locality in his usage pattern:
Spatial locality – if he reads a page in one book, the most likely page that he will read is the next page
Temporal locality - If he referenced something in one book, it is likely that he will reference it again

## Slide 6: Memory Hierarchy
Computers have varying levels of caches/memory.
Close to the CPU
Fast(est)
Smallest
Most Expensive ($)
Farthest from the CPU
Slow(est)
Largest
Least Expensive ($)
Registers
L1
L2
L3
Memory
SSD/HD

## Slide 7: Example: Ryzen 7 2700X
Memory Type | Size | Type | Latency | Cycles
Registers | 1KB | (8 X 16 register X 8 byte registers) | ~0 | ~0
L1 Cache (I) | 512KB | (8 X 64K, 4 way set assoc) | .95ns | ~4 cycles
L1 Cache (D) | 256KB | (8 X 32K, 8 way set assoc, write back) | .95ns | ~4 cycles
L2 Cache | 4MB | (8 X 512KB, 8 way set assoc, write back) | 3ns | 10.4 cycles
L3 Cache | 16MB | (2 X 8MB, 16 way set assoc) | 8.1ns | 30 cycles
Main Memory | ? GB |  | 66ns | 350 cycles

## Slide 8: Cache Hits and Misses
When a memory load is attempted, the hardware “looks in” L1 cache. If the address is not there, that is considered a miss.
The hardware will then look in L2. If L2 misses, the request goes to L3. If L3 misses, main memory must satisfy the request.
If a particular cache can satisfy the request, that is considered a cache hit.
When a block is read from lower in the cache hierarchy, the higher caches store it.

## Slide 9: How Do Hits and Misses Impact Run Time?
The CPU (in a simplified model – more on this later) must wait for a memory load to complete before continuing.
How do we compute memory stall cycles?

## Slide 10: Misses in the tiered hierarchy
If all memory accesses must be satisfied, some percentage of memory accesses will be satisfied by L1, some by L2, some by L3 and some by main memory.
The memory system must take the time to look in the cache whether the data is there or not.
If a value is not in any cache, for example, we still wait for L1, L2 and L3 to be checked. Why? Because we don’t know in advance where we might find any given value.

## Slide 13: Example:
If we have a 3ghz processor and we need to run 1 billion instruction, with an average of 2 cycles per instruction, we have:
Execution cycles = 1,000,000,000 * 2 c/I
2,000,000,000 cycles
3 ghz = 3,000,000,000 cycles per second
time = 2,000,000,000 / 3,000,000,000
time = 2/3 of a second.
This assumes a perfect cache that always has data ready for us.

## Slide 14: Example (continued)
Let’s assume that each cache level handles 90% of memory accesses and that in that 1,000,000,000 instructions, there were 1,200,000,000 memory accesses (don’t forget that instructions need to be loaded). We will use the numbers from the Ryzen 2700X above for timing.
For L1:
1,200,000,000 * .90 = 1,080,000,000 hits
Each attempt costs 4 cycles.
4,800,000,000 cycles
Remaining: 120,000,000

## Slide 15: Example (continued)
For L2, there are 120,000,000 memory attempts. 90% of those is 108,000,000. A cache attempt costs 10.4 cycles.
L2 cost is 1,248,000,000 cycles
L3, there are 12,000,000 memory attempts. 90% of those is 10,800,000. A cache attempt costs 30 cycles.
L3 cost is 360,000,000 cycles
Main memory will have to service the last 1,200,000 memory attempts. Main memory costs 350 cycles.
Main memory cost is 420,000,000 cycles.

## Slide 16: Example (conclusion)
Memory Stall Cycles =
L1: 4,800,000,000 cycles
L2: 1,248,000,000 cycles
L3: 360,000,000 cycles
Main: 420,000,000 cycles
Time = 2.943 seconds

## Slide 17: Stating the Obvious…
Memory accesses always hurt. Even with a 90% cache hit rate, they hurt a lot. Fortunately, 90% is considered AWFUL. Real rates are closer to 99%!
The only thing worse than a cache hit is a cache miss.
When possible, working from registers is a far better choice.

## Slide 18: Blocks
Caches work on the concept of blocks – consecutive sections of cache. A block of cache holds consecutive memory.
Bigger blocks means we swap out more at a time and have lower temporal locality.
Smaller blocks means that we spend a lot of time/hardware managing the mapping between memory and the block and we don’t take advantage of spatial locality.
The right size is a tradeoff of hit rate vs size.

## Slide 19: Improve Performance
How can we improve our performance?
Improve our hit rate
Reduce our miss penalty (remember, hits = 100% - misses)
Reduce the time that cache hits take

## Slide 20: How do misses happen?
The 3 C’s:
Compulsory – the block was never in the cache. We can’t do anything about this, really.
Capacity – the block was in the cache at one point, but we discarded it for space reasons
Conflict – 2 blocks conflict - let’s look at this

## Slide 21: Where can a block be placed in the cache?
So far, we have just considered the cache as a block of storage with some ideal mechanism – we put data in, we read data. Why is that a problem?
How do we find a block of data? If we know that we need address Q, how do we find it in the cache?

## Slide 22: Option 1: Fully Associative
Any block of memory can be stored anywhere. The cache stores the base of the address and the data.
For example – on a 32 bit machine, let’s assume that a block of memory is considered 1k for a certain cache. 1k = 210. So there is a “tag” of 22 bits indicating which 1k block of the memory is stored in this cache. This is known as the block address.
How do we perform a memory access? We have to compare the 22 bits of the address to each of the tags in the cache. That is a LOT of gates AND time for signal propagation. That takes a LONG time.

## Slide 23: Option 2: Direct Mapped
If searching every slot is slow, let’s not do that – let’s do the opposite:
Consider the block address from the previous example.
What if we took the block address MOD the number of blocks our cache will hold and that was the slot that we used? That would be super fast!
What’s the problem?
Hint – think back to Algorithms and Hash Tables

## Slide 24: Option 3: Set Associative
This is a hybrid approach:
Split the cache into S sets that hold N blocks.
Find the set by: Block Address MOD S (much like direct mapped)
Then look for our particular block amongst the N blocks (like fully associative)

## Slide 25: Let’s look at our Ryzen 2700X example
Memory Type | Size | Type
Registers | 1KB | (8 X 16 register X 8 byte registers)
L1 Cache (I) | 512KB | (8 X 64K, 4 way set assoc)
L1 Cache (D) | 256KB | (8 X 32K, 8 way set assoc, write back)
L2 Cache | 4MB | (8 X 512KB, 8 way set assoc, write back)
L3 Cache | 16MB | (2 X 8MB, 16 way set assoc)
If you know that this processor has 8 cores, divided into 2
blocks of 4, that explains a lot about the “Type” column

## Slide 26: Set Associativity Example
For the L1 data cache, let’s assume 64 byte blocks.
In 32kb, we can fit 512 blocks
This is an 8 way associative cache.
There are 64 (26)sets of 8.
As this is a 64 bit architecture:
The lowest 6 bits determine where in the block we are.
That means that our set determination takes 58 bits of address -> 16 bits of cache sets. If we had a full 264 bytes of memory, 4 trillion blocks would be competing for those 8. With “only” 16GB, 262,144 blocks are competing for those 8 blocks in the set, assuming all of those blocks are data blocks.

## Slide 27: Why split the instruction and data caches?
Instructions tend to be very consecutive. Data does not.
Different usage makes different cache design make sense.
Splitting them into two different “associativity” buckets is a good way to reduce collisions.
There are two different sources – a cache bank can only respond to one request at a time. Two banks means that data and instructions don’t wait for each other.
Instructions are needed at the start of the CPU’s process. Data is needed later.

## Slide 28: Prefetching
Instructions, in particular, have a very consistent pattern – the execution TENDS to start at the beginning and move toward the end.
If we know this, why not have the cache request the NEXT block of memory before this one is completely used?
Why might this backfire?

## Slide 29: Prefetching fails
Small methods that jump around
Data that is not contiguous
Frequent switching between processes
In spite of these, prefetching is still a huge win.

## Slide 30: Replacement Strategies
When a block is stored in the cache, if there is not an empty space, the controller has to make a decision about where to put the block.
For direct map, there are no options.
For 2 way, there are 2 options (0 or 1)
For 8 way, there are 8 options (0-7)
For fully associative, there are N options
How should it decide?

## Slide 31: Replacement Strategy Options
Random – surprisingly not a bad approach (why?)
Least Recently Used – track block usage, replace the block that hasn’t been touched in the longest time
First In-First Out – Approximates LRU

## Slide 32: What about writes?
The CPU reads FAR more than it writes (think about instructions).
When it DOES write, it probably doesn’t rewrite an entire cache block, so the process is complex.
Two approaches:
Write through: Data is written to the cache (if the block is in there) AND to main memory
Write back: Data is written to the cache ONLY. When the block is flushed from the cache, the data is written to main memory.

## Slide 33: Write-Through
Pros:
Easy to implement (no dirty indicator needed)
The cache is always equal to memory, so replacement is cheaper
All levels of cache that have data have the same version
Write-Back
Pros:
Writes happen at cache memory speed, not DRAM speed
Multiple writes to a block are cheaper
Saves power
Less memory contention

## Slide 34: Caching Roundup
We want to get the largest caches that we can
Cache takes space on the chip, so we can’t have all we want
Off chip cache isn’t worth doing
There are different strategies for deciding where in the cache data goes
There are different cache replacement strategies
There are different write strategies