## Slide 1: More Parallelism

## Slide 2: Some Taxonomy (Flynn’s)
Think about a CPU as a box that takes in instructions and data and yields results. Ignoring multi-core and SMP for a moment…
CPU/Core
Data
Instructions
Results

## Slide 3: Single Instruction Stream, Single Data Stream
A single instruction operates on a single stream. Most programming models work this way – it is natural to us.
But it’s not the only way.
Acronym: SISD

## Slide 4: Other Options
SIMD – Single instruction, multiple data
What we will talk about today
MISD – Multiple instruction, single data
Not really useful (spaceships need redundant calculations)
MIMD – Multiple Instructions, Multiple Data
This model is the multi-CPU, multi-core systems of today.

## Slide 5: Data Parallelism
It is not uncommon that we need to do the same operations on a lot of pieces of data:
for (a in array)
doSomething(a)
Examples: Image/sound/video processing, matrix operations, AI

## Slide 6: Key Concept
In order for code to be parallelizable, loop iterations must be independent.
for (int i=0;i<N;i++)
a[i] = a[i-1] + a[i-2];
This code is not vectorizable.

## Slide 7: Two Options
Array Processor – we have N ALUs. To process a batch (image, matrix, sound file, whatever), we break it up into N sections. We load N items. We do the operations on all N items. Then we save all N items out. Example – taking ALL of the laundry to the laundromat.
Vector Processor – we have 1 ALU. At time 0, we load item 0. At time 1, we load item 1 and process item 0. At time 2, we load item 2, process item 1 and store item 0. Essentially, we pipeline the items. Think of doing laundry at home with 1 washer and 1 dryer.
Tradeoffs?

## Slide 8: Vector processors sound like CPUs!
Some key differences:
By definition, there are no dependencies
With a known stride, we can accurately prefetch correctly
Never any branches (loop is inherent until all strides complete)
Short “programs” reduce the memory bandwidth pain – can live in cache?
Much simpler than the out of order, pipelined “normal” CPUs.
Result: very deep pipelines are OK

## Slide 9: Making a array processor
We need N*M registers to work on N items at a time.
M is the number of operands we can have.
Consider C[i] = A[i] + B[i]. We need 3 (M) registers for each N.
We need a few control registers:
VLEN – how many total data items we need to work on
VSTR – how many words between data items (stride)
VMASK – indicates which of the registers (bitwise) to work on.

## Slide 10: A note about memory
Because vector processors are deeply pipelined, they can issue a lot of load/store combinations in a short time and will very quickly saturate memory.
It is important that you divide your workload up so that elements (both load and store) are divided up among banks of memory.
The fastest processor that sits and waits for memory is no better than a brick.

## Slide 11: If only everything were quite this simple…
In some cases, there are data items used by more than 1 calculation.
For example, consider 1 dimensional blurring (2D is just an extension of the same idea). The value of o[j] = (i[j-1]+i[j] + i[j+1])/3 (o = output, i = input).
This is called chaining. Vector processors typically support it, but now we have a problem. We can’t pipeline. Why?

## Slide 12: Does the diagram help?
In[0]
In[1]
In[2]
Out[0]
Out[1]
Out[2]
Add
Div
Add
Div
Add
Div

## Slide 13: Memory can’t serve two (or three) masters
Typically, memory can only be read by one unit at a time
But multi-ported memory can be used.
In this case, we need 3 ported memory in order to pipeline this process fully.

## Slide 14: More “fun” with memory
What if we need to reference memory, but we want to either load or store indirectly: A[B[i]] = C[D[i]] + 1
This is called a scatter (output) and gather (input) operation.
There is hardware for this in most vector processors.

## Slide 15: A little more…
What if we want to only operate on certain data items?
A[i] = B[i] / C[i], if C[i] != 0
That’s what the VMASK is for.
We can mask out the records where C[i] is 0.
Does this remind you of something? Maybe from ARM?

## Slide 16: One more masking example
What if I want to do something like this:
if (a[i] > b[i])
c[i] = a[i]-b[i];
else
c[i] = b[i] – a[i];
Becomes:
VMASK = A>B
C = A-B
VMASK = !VMASK
C = B-A

## Slide 17: Loop Unrolling
You might remember this from 311…
for (int i=0;i<N;i++)
c[i] = a[i] + b[i];
can become:
for (int i=0;i<N;i+=4) {
c[i] = a[i] + b[i];
c[i+1] = a[i+1] + b[i+1];
c[i+2] = a[i+2] + b[i+2];
c[i+3] = a[i+3] + b[i+3];
}
Why do we (the compiler, really) do this? Because looping (branches, compares)
are overhead – “useful” work is not getting done.
Why don’t we unroll the loop completely (i.e. make N copies of the row)?

## Slide 18: Let’s think about a piece of simple code
for (int i=0;i<N;i++)
c[i] = a[i] + b[i];
Load
Load
Add
Store
Load
Load
Add
Store
Iteration 1
Iteration 2

## Slide 19: We can think about this as a simple in-order
Load
Load
Add
Store
Iteration 1
Load
Load
Add
Store
Iteration 2
Or out of order
Load
Load
Add
Store
Iteration 1
Load
Load
Add
Store
Iteration 2
This is, essentially, the CPU unrolling the loop for us

## Slide 20: Or a vector processor (SIMD)
LOAD A  V1
LOAD B  V2
ADD V1, V2  V3
STORE V3  C
Ignoring stride, masks, etc…

## Slide 21: Or a multi-core CPU
Load
Load
Add
Store
Load
Load
Add
Store
Iteration 1
Iteration 3N/4
Load
Load
Add
Store
Iteration N/4
Load
Load
Add
Store
Iteration 2N/4

## Slide 22: Execution Model
If we have SPMD (single program, multiple data), where can we execute it?
We have the best of all worlds with this case –
We can run it in a loop on an SISD
We can run it on MIMD (multi-core)
We can run it in a vector processor (SIMD)
Because it is the same code and we are applying it to many pieces of data, we can run it anywhere.
This model has another name:
SPMD: Single Program, Multiple Data

## Slide 23: GPUs
GPUs are SIMD, but they don’t use the “special” vector instruction model. They use a threading model.
A vector processor is a very specific “machine” – you set it up and it runs until it is done.
A GPU is more like a series of CPUs with threads – you can start threads, stop threads, etc. You can have different threads working on different programs, even.

## Slide 24: GPUs
Considering the last slide, how are GPUs, then, different from multi-core CPUs?
They have support for threads executing the same instruction at the same time. These threads are a “warp” or a wavefront. This is done dynamically (i.e. programmatically). Doing this creates a SIMD operation.
The size of the warp can be 1 to number of execution units.

## Slide 25: On A GPU
Load
Load
Add
Store
Iteration 1
Iteration 4
Iteration 2
Iteration 3
Load
Load
Add
Store
Load
Load
Add
Store
Load
Load
Add
Store
Warp 0
Warp 1
Warp 2
Warp 3
Time
All iterations are working on the same instruction at the same time if they are part of the same warp.

## Slide 26: Shader Core
PC, Mask
Instruction Cache
Decode
ALU
Fetch
ALU
Fetch
ALU
Fetch
ALU
Fetch
Data Cache
Writeback
When any thread is waiting for memory, all of the threads become unschedulable, waiting for memory accesses to complete.
This allows the GPU to make more effective use of the ALUs.

## Slide 27: Compare Vector Processor To GPU Processor
Waiting
Complete
Load
Load
Add
Store
Item 0
Item 1
Item 2
Item 3
Item 4
Item 5
Load
Load
Add
Store
Load
Load
Add
Store
Load
Load
Add
Store
Load
Load
Add
Store
Item 0
Item 1
Item 3
Item 2
Item 4
Item 5
Item 6
Item 7
Item 8
Item 9
Item 10
Item 11
Item 20
Item 21
Item 23
Item 22
Item 12
Item 13
Item 14
Item 15
Item 16
Item 17
Item 18
Item 19

## Slide 28: Dividing your program into warps
The bigger the warp, the more parallelism you get from having only a single PC/instruction decode
The bigger the warp, the more likely that you get a memory stall and your whole warp gets unscheduled until the memory access completes.

## Slide 29: Branch Divergence
What happens if you have a piece of code:
for (int i=0;i<N;i++)
if (b[i]> 0)
c[i] = a[i] + b[i];
else
c[i] = a[i] - b[i];

## Slide 30: Stack of execution
Your warp splits into 2 warps; some execute one path some execute the other. Then they come back together to become one warp again.
This is a lot like the vector mask, in that some data elements run for one warp and some run for another.
A stack is kept to track the threads of execution.

## Slide 31
for (int i=0;i<N;i++)
if (b[i]> 0)
c[i] = a[i] + b[i];
else
c[i] = a[i] - b[i];
Compare (1)
Add (2)
Subtract (3)
Complete (4)
Reconvene PC | Next PC | Active Mask
---- | 1 | 1111
4 | 2 | 1010
4 | 3 | 0101
Notice that we get less effectively done with this method for the amount of CPU time used

## Slide 32: Dynamic Warp Formation
What if the GPU could determine if A[i] > B[i] and group all of those into one set of warps and all of the A[i] <= B[i] into another warp.
That would mean that we don’t need branch divergence!
Compare (1)
Add (2)
Complete (4)
Compare (1)
Subtract (3)
Complete (4)

## Slide 33: Hardware constraints ruin our perfect plan…
Remember our shader hardware diagram:
PC, Mask
Instruction Cache
Decode
ALU
Fetch
ALU
Fetch
ALU
Fetch
ALU
Fetch
Data Cache
Writeback
All of our code runs in the ALU; the fetch is into registers.
We can’t just switch “lanes”.

## Slide 34: Parallelism wins out…
GPUs are designed to work on millions of data items.
The chances that there will be roughly the same amount of work for each slot increases as the number of data items increase, if there is no bias of selection.
No additional hardware is necessary to make this work better.

## Slide 35: More parallelism roundup
Vector processors are simplified “one at a time” pipelines.
Array processors are made up of many ALUs
GPUs are arrays of vector processors that use the simplified model to do a lot of simple work very quickly.