## Slide 1: Out Of Order Execution
A foolish consistency is the hobgoblin of little minds, adored by little statesmen and philosophers and divines. With consistency a great soul has simply nothing to do. He may as well concern himself with his shadow on the wall. Speak what you think now in hard words, and tomorrow speak what tomorrow thinks in hard words again, though it contradict every thing you said today.
(Ralph Waldo Emerson)

## Slide 2: Who schedules the instructions?
The compiler can schedule the instructions, to some degree, but what can it NOT know before hand?

## Slide 3: Who schedules the instructions?
The compiler can schedule the instructions, to some degree, but what can it NOT know before hand?
Memory latency
Cache contents (and therefore cache hits/misses)
Branch decisions
Anything determined at runtime

## Slide 4: Floating Point
One thing that we haven’t mentioned is floating point. Remember back in week 1 we talked about how numbers are represented in IEEE floating point format?
Sending those numbers through an integer ALU will not work. Floating point has to be done with a set of (similar) circuits that follow different rules. Think back to the process of calculating with numbers in scientific notation. How do you deal with the exponent and the mantissa? A different representation of numbers needs different circuits.

## Slide 5: An opportunity has arrived!
If we have to have different hardware for integer and floating point, doesn’t that mean that ½ of our hardware is sitting idle at any time?
Could we use that to make our CPU faster?
YES! In fact, we can do better than JUST that!

## Slide 6: Superscalar
A superscalar architecture can execute MORE THAN 1 instruction per cycle!
How is that possible? Read in many instructions, and execute them in parallel!
The Zen (Ryzen) block diagram
AGU == address generation unit

## Slide 7: VLIW
All of the hazards and delays that we have come across happen because there are no rules about machine code. Any valid instruction can come before or after any other, regardless of dependencies.
VLIW (Very Long Instruction Word) is a different approach. What if the machine language consisted of “groups” of operations? The assembly developer/compiler would be responsible for ensuring that the group was internally parallelizable.

## Slide 8: VLIW (continued)
If your CPU had 3 integer units, 2 load/store units and a floating point unit, each instruction would look like this:
(ADD R1  R2, R3; SUB R4 R2,R5; NOP; LOAD R6,$1234;NOP;MULT R8 R7, R9)
Integer Load/Store Floating Point
Harder to write the assembly language/assembler/code emitter, easier/cheaper/faster to make the CPU

## Slide 9: VLIW issues
Too many NOPs – the code didn’t have (or the compiler couldn’t find) parallelism
The generated code is tied to the particular microarchitecture (what if a new CPU design comes out?)
Because all of the instructions have to complete at the same time, any long instructions (memory accesses!) cause the whole set of instructions to stall

## Slide 10: VLIW in real life
Lots of embedded and special purpose chips are VLIW – DSPs, (some) graphics chips, media processors (the chip in your DVD/Blu-ray).
In the US, Intel created Itanium (IA-64). It didn’t go over well (the compilers were too hard to write).
Russia’s Elbrus chip is a VLIW.

## Slide 11: If VLIW doesn’t work (well), what should we do?
Instead of static dependency checking, we can do the dependency checking dynamically (in the CPU).
This works better, too, because:
VLIW doesn’t solve long load/store waits
Branches make the order of the code impossible to predict ahead of time.

## Slide 12: “Reorder them by dependency”
If I have:
ADD R1  R2, R3
ADD R2  R1, R4
ADD R7  R8, R9
We can see that instruction 2 depends on the result of instruction 1.
We can see that instruction 3 has nothing to do with 1 or 2.
Register renaming can’t rescue us, here.

## Slide 13: Another example
LOAD R1  $12345678
ADD R2  R3, R4
SUB R5  R6, R7
MUL R8  R9, R10
How far ahead would we need to get to “cover” an access to main memory?

## Slide 14: Cooking metaphor
If we were making a dinner, we want to serve appetizer, then the main course, then dessert.
Ideally, we would make the appetizer, then while it is being eaten, we make the main course, etc.
But if the appetizer requires 3 hours to chill, we will have a lot of “stalls” at our dinner.
What if we reorder so that we make the appetizer and start it chilling, then make the main course and dessert? When the appetizer is done, we can serve it and then finish the other cooking (whatever isn’t done).

## Slide 15: A simple algorithm
We can proceed onto a new instruction if no pending instruction outputs its source(s).
If we have:
LOAD R1  $12345678
ADD R2 R1,R3 – we clearly can’t do this until the load comes back

## Slide 16: The hard part is memory
We can’t make a “memory file” – memory is too big AND the CPU isn’t the only system that can read/write to it.
Often, too, we calculate memory addresses.
Example:
if (x>0) myPerson = person1 else myPerson = person2;
age = myPerson.age;  age is located at myPerson + offset

## Slide 17: Caches make it even worse
load R1  $12345678
load R2  $23456780
Assuming that they are both started via out of order execution, which one will finish first?
Now what if we have a store to one of those addresses?

## Slide 18: Worse yet…
store $12345678  R1
add R2  R3,R4
load R3  $12345678
the store could still be working. How do we make sure that the load gets the right data?

## Slide 19: Easy, dumb approach
Wait for all stores to complete before allowing a load to occur.
We will wait unnecessarily, but we know that we are right and it takes very little hardware to build.

## Slide 20: Slightly harder
Check the addresses of all pending stores to make sure that none of them match our load.
What if we have this:
load R1  $12345678
addi R2  R1, #16
store (R2)  R3
load R4  $23456780 – this happens to be what R2 will be…

## Slide 21: Aggressive
Assume that you will never have a store-load collision, but then check if you DID and redo the work.
Complex to redo the work, requires rework (lose efficiency).

## Slide 22: Get smarter
Chose the aggressive path, with one slight change.
When we have to go back and redo work, create a cache of store locations that caused the rework.
Next time, check to see if there is any instruction in the cache that is a pending store. If so, wait for it before performing our load.

## Slide 23: What if we get stuck?
At some point, we could be waiting for memory operations to complete such that we can’t move forward.
What if we had *2* register files? We could “lie” to the operating system and tell it that we are actually *2* CPUs. When one “CPU” is tied up waiting for memory, the “other” CPU could do useful work.

## Slide 24: Hyperthreading
SUN (now owned by Oracle) came up with the idea – let’s duplicate some of the state hardware like program counter and have the CPU look like 2 CPUs!
Those 2 CPUs will share the units. The operating system will run processes on each CPU and hopefully their work loads will balance out.

## Slide 25: Exceptions
What happens if something breaks in this process? Examples include arithmetic overflow, an undefined opcode, or a bad address?
A CPU exception happens and the processor jumps to a known address where (presumably) there is code to recover.
Some CPUs have “precise” exceptions – the state of the CPU is updated so that there is no partially completed work. An imprecise exception CPU does not do this update and the interrupt handler needs to deal with this. Pros/cons?

## Slide 26: Superscalar and Out of order conclusion
Executing more than one instruction at a time is a huge performance win.
It’s also hard to do and requires a lot of effort and circuitry to ensure that the CPU is consistent, with precise exceptions.